## Slide 1
The objective of this tutorial is to implement basic L3 forwarding.
To keep the exercise small, we will just implement forwarding for IPv4.
With IPv4 forwarding, the switch must perform the following actions for every packet:
(i) update the source and destination MAC addresses,
(ii) decrement the time-to-live (TTL) in the IP header, and
(iii) forward the packet out the appropriate port.
Your switch will have a single table, which the control plane will populate with static rules.
Each rule will map an IP address to the MAC address and output port for the next hop.
We have already defined the control plane rules, so you only need to implement the data plane logic of your P4 program.
mininet> nodes
available nodes are:
h1 h2 h3 s1 s2 s3
mininet> links
h1-eth0<->s1-eth1 (OK OK)
h2-eth0<->s2-eth1 (OK OK)
h3-eth0<->s3-eth1 (OK OK)
s1-eth2<->s2-eth2 (OK OK)
s1-eth3<->s3-eth2 (OK OK)
s3-eth3<->s2-eth3 (OK OK)
mininet>

## Slide 2
S1
S3
H1
H2
H3
Eth0: 10.0.1.10 : 00:04:00:00:00:01
Eth1 00:aa:00:01:00:01
eth3
Eth0 10.0.3.10 : 00:04:00:00:00:03
Eth1 00:aa:00:02:00:02
Eth0 10.0.2.10 : 00:04:00:00:00:02
eth3
eth2
eth2
eth3
eth2
Eth1 00:aa:00:03:00:03
S3
S2
S1
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => 00:aa:00:01:00:01 1
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => f2:ed:e6:df:4e:fa 2
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => f2:ed:e6:df:4e:fb 3
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => 00:aa:00:02:00:02 1
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => 22:a8:04:41:ab:d3 2
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => 22:a8:04:41:ab:d4 3
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => 00:aa:00:03:00:01 1
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => f2:ed:e6:df:4e:fb 2
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => f2:ed:e6:df:4e:fa 3
H1-> H2
Src 10.0.1.10
Dest 10.0.2.10 : src mac : 00:04:00:00:00:01
Dstmac : 00:aa:00:01:00:01
S1  P4 program – parser ; ingress ; apply ()
Table 10.0.2.10/32 => f2:ed:e6:df:4e:fa 2
Ipv4_forward ()
Egress port 2 (eth2)
Dstmac (00:aa:00:01:00:01) set it as Srcmac
Set Destmac as f2:ed:e6:df:4e:fa
S1 -> S2
Src 10.0.1.10
Dest 10.0.2.10 : Src mac : 00:aa:00:01:00:01
Dstmac : f2:ed:e6:df:4e:fa
S2  P4 program – parser ; ingress ; apply ()
Table 10.0.2.10/32 => 00:aa:00:02:00:02 1
Ipv4_forward ()
Egress port 1 (eth1)
Dstmac (f2:ed:e6:df:4e:fa) set it as Srcmac (f2:ed:e6:df:4e:fa)
Set Destmac as 00:aa:00:02:00:02

## Slide 3
H1-> H2
Src 10.0.1.10
Dest 10.0.2.10
H1  S1
S1 parse packet  checksum  ingress  extract the ipv4 address & do table match
Dest Ip match  insert the Dest MAC & Egress port
f2:ed:e6:df:4e:fa 2
SENDER SIDE : H1
sending on interface h1-eth0 to 10.0.2.10
###[ Ethernet ]###
dst = ff:ff:ff:ff:ff:ff
src =
type = 0x800:04:00:00:00:0100
###[ IP ]###
version = 4L
ihl = 5L
tos = 0x0
len = 38
id = 1
flags =
frag = 0L
ttl = 64
proto = udp
chksum = 0x63b3
src = 10.0.1.10
dst = 10.0.2.10
\options \
###[ UDP ]###
sport = 1234
dport = 4321
len = 18
chksum = 0x1c6a
###[ Raw ]###
load = 'P4 is cool'
RECEIVER SIDE : H2
sniffing on h2-eth0
got a packet
###[ Ethernet ]###
dst = 00:aa:00:02:00:02
src = f2:ed:e6:df:4e:fa
type = 0x800
###[ IP ]###
version = 4L
ihl = 5L
tos = 0x0
len = 38
id = 1
flags =
frag = 0L
ttl = 62
proto = udp
chksum = 0x65b3
src = 10.0.1.10
dst = 10.0.2.10
\options \
###[ UDP ]###
sport = 1234
dport = 4321
len = 18
chksum = 0x1c6a
###[ Raw ]###
load = 'P4 is cool'
Intermediate Layer 2 Switch S1
sniffing on s1-eth1
got a packet
###[ Ethernet ]###
dst = ff:ff:ff:ff:ff:ff
src = 00:04:00:00:00:01
type = 0x800
###[ IP ]###
version = 4L
ihl = 5L
tos = 0x0
len = 38
id = 1
flags =
frag = 0L
ttl = 64
proto = udp
chksum = 0x63b3
src = 10.0.1.10
dst = 10.0.2.10
\options \
###[ UDP ]###
sport = 1234
dport = 4321
len = 18
chksum = 0x1c6a
###[ Raw ]###
load = 'P4 is cool'
Intermediate Layer 2 Switch S2
sniffing on s2-eth2
got a packet
###[ Ethernet ]###
dst = f2:ed:e6:df:4e:fa
src = ff:ff:ff:ff:ff:ff
type = 0x800
###[ IP ]###
version = 4L
ihl = 5L
tos = 0x0
len = 38
id = 1
flags =
frag = 0L
ttl = 63
proto = udp
chksum = 0x64b3
src = 10.0.1.10
dst = 10.0.2.10
\options \
###[ UDP ]###
sport = 1234
dport = 4321
len = 18
chksum = 0x1c6a
###[ Raw ]###
load = 'P4 is cool'

## Slide 4
Configuring switch... s1
table_set_default ipv4_lpm drop
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => 00:aa:00:01:00:01 1
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => f2:ed:e6:df:4e:fa 2
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => f2:ed:e6:df:4e:fb 3
Obtaining JSON from switch...
Done
Control utility for runtime P4 table manipulation
RuntimeCmd: Setting default action of ipv4_lpm
action: drop
runtime data:
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:01:0a/32
action: ipv4_forward
runtime data: 00:aa:00:01:00:01 00:01
Entry has been added with handle 0
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:02:0a/32
action: ipv4_forward
runtime data: f2:ed:e6:df:4e:fa 00:02
Entry has been added with handle 1
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:03:0a/32
action: ipv4_forward
runtime data: f2:ed:e6:df:4e:fb 00:03
Entry has been added with handle 2
RuntimeCmd:
Configuration complete.
Configuring switch... s2
table_set_default ipv4_lpm drop
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => 00:aa:00:02:00:02 1
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => 22:a8:04:41:ab:d3 2
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => 22:a8:04:41:ab:d4 3
Obtaining JSON from switch...
Done
Control utility for runtime P4 table manipulation
RuntimeCmd: Setting default action of ipv4_lpm
action: drop
runtime data:
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:02:0a/32
action: ipv4_forward
runtime data: 00:aa:00:02:00:02 00:01
Entry has been added with handle 0
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:01:0a/32
action: ipv4_forward
runtime data: 22:a8:04:41:ab:d3 00:02
Entry has been added with handle 1
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:03:0a/32
action: ipv4_forward
runtime data: 22:a8:04:41:ab:d4 00:03
Entry has been added with handle 2
RuntimeCmd:
Configuring switch... s3
table_set_default ipv4_lpm drop
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => 00:aa:00:03:00:01 1
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => f2:ed:e6:df:4e:fb 2
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => f2:ed:e6:df:4e:fa 3
Obtaining JSON from switch...
Done
Control utility for runtime P4 table manipulation
RuntimeCmd: Setting default action of ipv4_lpm
action: drop
runtime data:
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:03:0a/32
action: ipv4_forward
runtime data: 00:aa:00:03:00:01 00:01
Entry has been added with handle 0
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:01:0a/32
action: ipv4_forward
runtime data: f2:ed:e6:df:4e:fb 00:02
Entry has been added with handle 1
RuntimeCmd: Adding entry to lpm match table ipv4_lpm
match key: LPM-0a:00:02:0a/32
action: ipv4_forward
runtime data: f2:ed:e6:df:4e:fa 00:03
Entry has been added with handle 2
RuntimeCmd:

## Slide 5
V1Switch(
ParserImpl(), =======================> Parser Function
verifyChecksum(),
ingress(),
egress(),
computeChecksum(),
DeparserImpl()
) main;
parser ParserImpl(packet_in packet,
out headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) {
state start {
transition parse_ethernet;
}
state parse_ethernet {
packet.extract(hdr.ethernet);
transition select(hdr.ethernet.etherType) {
TYPE_IPV4: parse_ipv4;
default: accept;
}
}
state parse_ipv4 {
packet.extract(hdr.ipv4);
transition accept;
}
}
A P4 parser describes a state machine with one start state and two final states. The start state is always named start.
The two final states are named accept (indicating successful parsing) and reject (indicating a parsing failure).
The start state is part of the parser, while the accept and reject states are distinct from the states provided by the programmer and are logically outside of the parser.
control ingress(inout headers hdr, inout metadata meta, inout standard_metadata_t standard_metadata) {
/* This action will drop packets */
action drop() {
mark_to_drop();
}
action ipv4_forward(macAddr_t dstAddr, egressSpec_t port) {
/*
* TODO: Implement the logic to:
* 1. Set the standard_metadata.egress_spec to the output port.
* 2. Set the ethernet srcAddr to the ethernet dstAddr.
* 3. Set the ethernet dstAddr to the dstAddr passed as a parameter.
* 4. Decrement the IP TTL.
* BONUS: Handle the case where TTL is 0.
*/
}
table ipv4_lpm {
key = {
/* TODO: declare that the table will do a longest-prefix match (lpm)
on the IP destination address. */
}
actions = {
/* TODO: declare the possible actions: ipv4_forward or drop. */
NoAction;
}
size = 1024;
default_action = NoAction();
}
apply {
/* TODO: replace drop with logic to:
* 1. Check if the ipv4 header is valid.
* 2. apply the table ipv4_lpm.
*/
drop();
}
}
LPM match based the key ==> ipv4_forward
Drop
ipv4_forward ==> egress port ==> input
ethernet srcaddress (mac) ===> as ethernet
* 1. Set the standard_metadata.egress_spec to the output port. ==> Set egress port
* 2. Set the ethernet srcAddr to the ethernet dstAddr. ==> Packet dstaddr put it srcaddres
* 3. Set the ethernet dstAddr to the dstAddr passed as a parameter. ==> Table match mac 'dstAddr' to ethernet dstaddr

## Slide 6
S1
S3
H1
H2
H3
Eth0: 10.0.1.10 : 00:04:00:00:00:01
Eth1 00:aa:00:01:00:01
Eth0 10.0.3.10 : 00:04:00:00:00:03
Eth1 00:aa:00:02:00:02
Eth0 10.0.2.10 : 00:04:00:00:00:02
Eth3 00:bb:00:01:00:02
Eth2 00:bb:00:01:00:01
Eth2 00:cc:00:01:00:02
Eth2 00:dd:00:01:00:02
Eth1 00:aa:00:03:00:03
S3
S2
S1
H1-------------> H2
H1
Src 10.0.1.10 src mac : 00:04:00:00:00:01
Dest 10.0.2.10 : dst mac : ff:ff:ff:ff:ff:ff
Egress port = eth0
S1
Src ip <> src mac : 00:bb:00:01:00:01
Dest 10.0.2.10 : dst mac : ff:ff:ff:ff:ff:ff
Egress port = eth2
Ttl decrement
S2
Src ip <> src mac : 00:aa:00:02:00:02
Dest 10.0.2.10 : dst mac : ff:ff:ff:ff:ff:ff
Egress port = eth 1
Eth3 00:cc:00:01:00:03
Eth3 00:dd:00:01:00:03
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => 00:bb:00:01:00:01 2
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => 00:aa:00:01:00:01 1
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => 00:bb:00:01:00:02 3
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => 00:aa:00:02:00:02 1
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => 00:cc:00:01:00:02 2
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => 00:cc:00:01:00:03 3
table_add ipv4_lpm ipv4_forward 10.0.2.10/32 => 00:dd:00:01:00:03 3
table_add ipv4_lpm ipv4_forward 10.0.1.10/32 => 00:dd:00:01:00:02 2
table_add ipv4_lpm ipv4_forward 10.0.3.10/32 => 00:aa:00:03:00:03 1

## Slide 7
S1
H2
H1
ARP Req
ARP Rsp
H1 pinging h2
At h1
Srcip = h1_eth1_ip src mac = h1_eth_mac
Destip = h2 ip DestMAC = ff:ff
At S1
s1-eth2
s1-eth1
h1-eth0 10.0.0.10 00:04:00:00:00:00
Default Route 10.0.0.1 (00:aa:bb:00:00:00)
h2-eth0 10.0.1.10 00:04:00:00:00:01
Default route to switch: 10.0.1.1 (00:aa:bb:00:00:01)
s1-eth1 Link encap:Ethernet HWaddr 52:bc:fd:e5:a8:92
inet6 addr: fe80::50bc:fdff:fee5:a892/64 Scope:Link
UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
RX packets:1 errors:0 dropped:0 overruns:0 frame:0
TX packets:28 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:1000
RX bytes:90 (90.0 B) TX bytes:3254 (3.2 KB)
s1-eth2 Link encap:Ethernet HWaddr a2:4a:15:b3:68:ff
inet6 addr: fe80::a04a:15ff:feb3:68ff/64 Scope:Link
UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
RX packets:1 errors:0 dropped:0 overruns:0 frame:0
TX packets:28 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:1000
RX bytes:90 (90.0 B) TX bytes:3254 (3.2 KB)
h1-eth0
h2-eth0
Notes: Adding host h1
Adding host h2
*** Creating network
*** Adding hosts:
h1 h2
*** Adding switches:
s1
*** Adding links:
(h1, s1) (h2, s1)
*** Configuring hosts
h1 h2
*** Starting controller
*** Starting 1 switches
s1 Starting P4 switch s1.
simple_switch -i 1@s1-eth1 -i 2@s1-eth2 --pcap --thrift-port 9090 --nanolog ipc:///tmp/bm-0-log.ipc --device-id 0 arp.p4.json --log-console
P4 switch s1 has been started.
**********
Network configuration for: h1
Default interface: h1-eth0 10.0.0.10 00:04:00:00:00:00
Default route to switch: 10.0.0.1 (00:aa:bb:00:00:00)
**********
**********
Network configuration for: h2
Default interface: h2-eth0 10.0.1.10 00:04:00:00:00:01
Default route to switch: 10.0.1.1 (00:aa:bb:00:00:01)
**********
Reading switch configuration script: simple_router.config
Configuring switch...
Obtaining JSON from switch...
Done
Control utility for runtime P4 table manipulation
RuntimeCmd: Error: Table ipv4_lpm has no action set_dst_info
RuntimeCmd:
Configuration complete.

## Slide 8
Address Resolution Protocol (request)
Hardware type: Ethernet (1)
Protocol type: IP (0x0800)
Hardware size: 6
Protocol size: 4
Opcode: request (1)
Sender MAC address: Cisco_08:65:46 (00:26:98:08:65:46)
Sender IP address: 20.20.20.24 (20.20.20.24)
Target MAC address: Broadcast (ff:ff:ff:ff:ff:ff)
Target IP address: 20.20.20.20 (20.20.20.20)
n7k-01-ANYCAST-vdc-5(config-if-hsrp)# show interface vlan 20
Vlan20 is up, line protocol is up, autostate enabled
Hardware is EtherSVI, address is 0026.9808.6546
Internet Address is 20.20.20.24/24
Address Resolution Protocol (reply)
Hardware type: Ethernet (1)
Protocol type: IP (0x0800)
Hardware size: 6
Protocol size: 4
Opcode: reply (2)
Sender MAC address: Cisco_08:65:47 (00:26:98:08:65:47)
Sender IP address: 20.20.20.20 (20.20.20.20)
Target MAC address: Cisco_08:65:46 (00:26:98:08:65:46)
Target IP address: 20.20.20.24 (20.20.20.24)
n7k-01-ANYCAST-vdc-6# show int vlan 20
Vlan20 is up, line protocol is up, autostate enabled
Hardware is EtherSVI, address is 0026.9808.6547
Internet Address is 20.20.20.20/24

## Slide 9
[Protocols in frame: eth:ip:icmp:data]
Ethernet II, Src: Cisco_08:65:46 (00:26:98:08:65:46), Dst: Cisco_08:65:47 (00:26:98:08:65:47)
Destination: Cisco_08:65:47 (00:26:98:08:65:47)
Address: Cisco_08:65:47 (00:26:98:08:65:47)
.... ..0. .... .... .... .... = LG bit: Globally unique address (factory default)
.... ...0 .... .... .... .... = IG bit: Individual address (unicast)
Source: Cisco_08:65:46 (00:26:98:08:65:46)
Address: Cisco_08:65:46 (00:26:98:08:65:46)
.... ..0. .... .... .... .... = LG bit: Globally unique address (factory default)
.... ...0 .... .... .... .... = IG bit: Individual address (unicast)
Type: IP (0x0800)
Internet Protocol Version 4, Src: 20.20.20.24 (20.20.20.24), Dst: 20.20.20.20 (20.20.20.20)
Protocol: ICMP (1)
Type: 8 (Echo (ping) request)
Ethernet II, Src: Cisco_08:65:47 (00:26:98:08:65:47), Dst: Cisco_08:65:46 (00:26:98:08:65:46)
Destination: Cisco_08:65:46 (00:26:98:08:65:46)
Address: Cisco_08:65:46 (00:26:98:08:65:46)
.... ..0. .... .... .... .... = LG bit: Globally unique address (factory default)
.... ...0 .... .... .... .... = IG bit: Individual address (unicast)
Source: Cisco_08:65:47 (00:26:98:08:65:47)
Address: Cisco_08:65:47 (00:26:98:08:65:47)
.... ..0. .... .... .... .... = LG bit: Globally unique address (factory default)
.... ...0 .... .... .... .... = IG bit: Individual address (unicast)
Type: IP (0x0800)
Internet Control Message Protocol
Type: 0 (Echo (ping) reply)
ICMP responses

## Slide 10: Arp.p4